## Slide 1: Arm Cortex Architect
Apr 14, 2024

## Slide 2: 1. Environment - Installation
Window 11 Pro 64-bit (10.0, Build 22631)
Arm GNU Toolchain Version 13.2.Rel1: arm_gnu_link
gdb-multiarch-14.1: gdb_link
qemu-20240411: qemu_link
Musca-board b1 bare-metal project: Musca_link
GnuMake: gnumake_link

## Slide 3: 2. GDB
Command | Description
run or r | Executes the program from start to end.
break or b | Sets a breakpoint on a particular line.
disable | Disables a breakpoint
enable | Enables a disabled breakpoint.
next or n | Executes the next line of code without diving into functions.
step | Goes to the next instruction, diving into the function.
list or l | Displays the code.
print or p | Displays the value of a variable.
quit or q | Exits out of GDB.
clear | Clears all breakpoints.
continue | Continues normal execution
info b, info r | Displays information of a breakpoint or a register

## Slide 4: 3. Musca B1 bare metal sample project

## Slide 5: 4. Processor core, processor and microcontroller

## Slide 6: 5. Operational modes of the Cortex-Mx processor
Type:
  Thread mode
  Handler mode
All your applications code will be executed under "Thread mode" of the processor. This is also called as "User Mode“.
Processor always starts with "Thread mode"
Whenever the core meets with the system exception or any external interrupts then the core will change its mode to handler mode in order to service the ISR associated with that system exception or the interrupt.

## Slide 7: 6. Access levels
Types:
  Privileged level (PAL)
    Full access to processor resources
    Handler mode is always privileged
    Thread mode is by default privileged, but can be changed to non-privileged
  Non-privileged level (NPAL)
    Restricted access
    You can make thread mode to run in this level
You can use the CONTROL register of the processor if you want to switch between the access level

## Slide 8: 7. Core register

## Slide 9: 8. Memory mapped and non memory mapped registers of the microcontroller
The registers do not have unique addresses to access them. Hence, they are not part of the processor memory map
You cannot access these registers in a C program using address dereferencing
To access these register in C, you have to use assembly instruction
Every register has its address in the processor memory map
You can access these registers in a C program using address dereferencing
Non-memory mapped registers
Register of the processor specific peripherals (NVIC, MPU, SCB, DEBUG, etc)
Register of the microcontroller specific peripherals (RTC, I2C, TIMER, CAN, USB, etc)
Memory mapped registers

## Slide 10: 9. ARM GCC inline assembly code
Inline assembly code is used to write pure assembly code inside a C program

## Slide 11: 9. ARM GCC inline assembly code (cont)
Extended form of an inline assembler statement: refer link
__asm volatile (“MOV R0, R1”);
__asm volatile (“MOV R0, R1”:::);
__asm volatile (code : output operand list : input operand list : clobber list);
Each input and output operand is described by a constraint string followed by a C expression in parentheses
Input/output operand format:
“<Constraint strings>” (< C expression >)
Example 1: Move the content of C variable into Arm register R0
Example 2: Move the content of R0 register into C variable